Gionata Boccalini

# SmartLamp: communication protocol

Communication protocol between micro and BLE module. The communication is made through a serial line at 9600 baud.
COMMANDS (BLE → micro):
1. ST_YYYYMMDD_hhmmss: sets the date and time from Android to the RTC;
2. AL_WD_hhmm_mm_rrr_ggg_bbb: sets an alarm on the weekday WD, hour and minute, with the specified fadetime [minutes], and color [RGB format]. The fadetime and color are optional.
3. AL_WD_hhmm: sets an alarm on the weekday WD, hour and minute;
4. AL_DIS_WD: disable alarm on the weekday WD;
5. FT_WD_mm: set the lamp fade time in minutes, after the alarm, [0, 99];
6. RGB_RRR_GGG_BBB: LED test mode with the specified RGB color.
7. OPT_TO_BBR: options:
  1. TO: time on after fadetime, in minutes, [0, 99];
  2. BBR: LED brightness [1, 100%]: 0 → defautl value 50 %
8. TEST: alarm test mode: starts the alarm of the current day.
9. PRINT: print the current time and alarms on the serial interface.
10. EXIT: exit from all command mode.

ACKs (micro → BLE):
OK: the micro sends back ‘OK’ as acknowledge;